Survey No. 1003-1849-1s

# SURVEY, CONDITION AND INSPECTION REPORT

This survey reports the condition of the vessel including hull, machinery equipment, fittings and outfit to the best of our knowledge without removing the paneling, ceiling, bulkheads or other parts of her structure and without internal examination of engines and machinery. This report represents our true and unbiased opinion of the Survey but in no event is this report to be considered a guarantee. Neither this office nor the undersigned Surveyor shall be liable in damages of any nature whatsoever for any errors of judgment, omissions or mistakes in making this survey and report.

SPECIFIC INFORMATION

| NAME OF VESSEL | “JUST PERFECT” Doc. #1038443 | DATE | October 9, 2003 |
| --- | --- | --- | --- |
| TYPE | Formula F-382 SR1 | SURVEYED FOR | Carol Cedeno |
| NUMBER | TNRD5262F596 FL 3859 LT | ADDRESS | 339 Maria Drive |
| BUILDER | Thunderbird Products | CITY, STATE | Toms River, NJ 08753 |
| WHERE BUILT | Decatur, Indiana | SURVEYED AT | Pompano Beach, Florida |
| YEAR BUILT | 1996 | AFLOAT | Yes | HAULED | Yes | UNDERWATER SURVEY | no |
| L.O.A. | 38’ | L.W.L. | - | BEAM | 8’3” | DRAFT | 3’ | CLEARANCE | - |
| NET WT. | 10,450# | GROSS WT. | - | TYPE OF CONSTRUCTION | Molded fiberglass |

MAIN ENGINES

| MODEL | MerCruiser HP 500 | TYPE | I/o | COOLING | Fresh water | H.P. | 470 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| SERIAL NO. PORT | OF 213580 | STARBOARD | Unknown | CYLINDERS | 8.2L V-8 |
| TRANSMISSION | - | REDUCTION | 1.50:1 | SHAFT | Bravo 1 | PROPELLER | 25” P Mirage |

ELECTRONIC EQUIPMENT

| SHIP TO SHORE | - | DEPTHOMETER | Lowrance 3500 digital |
| --- | --- | --- | --- |
| AUTO PILOT | - | RADAR | - |
| GPS | Northstar 951X GPS | OTHER | Kenwood stereo with CD |

AUXILIARY EQUIPMENT

| BILGE PUMP | 2000 GPH Rule with auto | GENERATOR | - |
| --- | --- | --- | --- |
| WATER HEATER | Atwood 6 gallon electric | REFRIGERATOR | Norcold DE 351D AC/DC |
| AIR CONDITIONER | - | STOVE | Panasonic microwave oven |

ANCILLARY INFORMATION

| PURPOSE OF VESSEL | pleasure | WATERS NAVIGATED | coastal & nearby islands |
| --- | --- | --- | --- |
| EXPERIENCE OF SKIPPER OR OWNER | Unknown | CREW REQUIRED | 1 |

VALUATIONS

| REPLACEMENT | $255,000 | BOAT VALUE | $98,050 | EQUIP. | INCL. | PRES. VALUE | $98,050 |
| --- | --- | --- | --- | --- | --- | --- | --- |

### SOUTHEAST FIRE AND MARINE ASSOCIATES, INC

### Page 5 of 7                                                                                                                               Survey No. 1003-1849-1s

SEA TRIAL

###### Port Engine                                                          Starboard Engine

252 hours						    251 hours

|  | RPM | WATER TEMP. | OIL PRES. | VOLTS |  |  | RPM | WATER TEMP. | OIL PRES. | VOLTS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SLOW | 650 | - | 45 | 12.8 |  | SLOW | 650 | - | - | - |
| HALF | - | - | - | - |  | HALF | - | - | - | - |
| CRUISE | - | - | - | - |  | CRUISE | - | - | - | - |
| FULL | 3000 | - | 55 | 13.8 |  | FULL | 3000 | 160 | 58 | - |

PERFORMANCE

Port engine runs rough – idles poorly and black smoke from exhaust.  Starboard engine seems okay – cannot perform proper Sea Trial with port engine down on power

REMARKS

- Port temperature gauge not working.

- Port carburetor dumping too much fuel – spark plugs fouled.

- Exhaust manifolds and tailpipes leaking on each engines’ port cylinder bank.

- Port engine needs rear motor mounts and realign engine.

- Port outdrive has oil in bellows – may need new upper seal.

ADDENDUM – 10/28/03

Port engine was removed from boat and repaired after successful compression check.  Tailpipes were welded and gaskets were replaced.  Circulating pump was replaced, as were spark plugs in both engines.  Boat is due for follow-up Sea Trial.

The compass was sent out for reconditioning and both power valves were replaced in the carburetors.  All gauges and senders are being replaced with new Gaffrig.